## Slide 1: The Multi-semantics of Addressing
Stewart Bryant
Futurewei (US) & University of Surrey (UK)
sb@stewartbryant.com
IETF FIPE Side Meeting July 2020

## Slide 2: What is an Address
For the purposes of this talk it is the part(s) of the packet that is used to steer the packet over the network to the process that needs the packet delivered to it.
For the purposes of the talk it is the contents of the field called “address” or “label”.
The term is generally associated with the endpoint of a layer 2 or layer 3 delivery.
As far as the application is concerned the session identifier is often the real “address”, and all that the network layer address provides is an instruction on how/where to deliver the packet over the current temporary packet transports at network layer.

## Slide 3: Types of address
The IETF deals primarily with the following types of addresses
  IEEE 802 MAC addresses
  IPv4
  IPv6
  MPLS label
  E164
At the network layer we map every address behavior to one of these address types and live with the constraints that brings.
We tend to build underlays (packet transport networks), overlays and applications using the same address types.
Source address is the same format as destination address.
There is a trend towards compressed addresses.

## Slide 4
node
many
(all in a set)
paths
content
service
identify
locate
instruct
secure
many
(ordered, e.g. segments)
WHAT
CARDINALITY*
FUNCTION
The evolving scope of addresses
one
*some at a meta-level, i.e. how to get there
Over the years, people have evolved more and more ideas of what to include in the meaning of an address
Interface

## Slide 5: Scope of an Address
The fundamental scope is that it need to be understood only by the set of nodes that need to process it.
  A node that will never see a packet does not need to know anything about its address.
  A node that processes a packet should never give it to a node that does not understand it.
  A node that receives a packet it does not understand should not attempt to process it.
That very much sets the scope of the nodes that need to understand an address and gives us a lot of freedom in terms of the design and development of the addressing scheme.

## Slide 6: Instructions
An instruction is something that the packet tells the forwarding layer about the handling of the packet.
It does this in conjunction with some parameters.
  Instruction – deliver this packet to foo.
  Parameter – use this CoS. Don’t go more than x hops from here.
MPLS introduced more complex instructions:
  Look the packet up in this VPN (RFC2547).
  Decapsulate and send out this interface (PW).
SR introduced a sequence of instructions.
Instructions can be transparent or opaque

## Slide 7: Network Programming
SRv6 Network Programming took advantage of the size of IPv6 addresses and longest match lookup to encode two instructions in an address:
  Deliver the packet to <prefix>
  Now carry out instruction<suffix>
This in effect shortened the delivery instruction implicit in any conventional network layer address and added supplementary instruction as a suffix.
Because of longest match the packet will be delivered to its target using the address prefix, and the target will understand how to process the suffix instruction. *
SR is publishing the suffix encoding so that it is a transparent instruction.
This approach allows instructions to be carried out on path by nodes other than the delivery target.
* Another way of viewing this is to consider that the target has a huge number of addresses

## Slide 8: Table-driven networking
The direction that the evolution of the network layer address has taken us is towards table-driven networking.
This is a paradigm in which the mapping between an identifier in the packet and an instruction pre-loaded into the forwarding plane and is provided by the control system (Routing protocol, SDN controller etc).
In this approach new forwarding behaviors are added to the network not by the construction of a new protocol, but instead by the introduction of new procedures into the forwarding plane h/w & f/w and the packet constructed in such a was as to vector the forwarding processor to the required behavior.

## Slide 9: Transparency <-> Opacity Spectrum
An address is transparent if anyone inspecting it can fully interpret it.
  This is the case for “classic” IP addresses.
An address is transparent within a domain if any entity within that domain can interpret it, but an entity outside that domain cannot.
  This is the case with NAT.
An address is opaque if only the next processing entity can interpret it.
  An MPLS “normal” label.

## Slide 10
Location
Identifier
Function(s)
Type of
Thing
Security
collateral
Function
parameters
Address
Address
Address
Address
From semantic overloading to opacity
Over time, aspects included in an address have grown
Many could be carried in separate fields, but for various reasons were squeezed into addresses
Limiting factors: 128 bit real estate, need for major standardization effort for each extension
Location
Identifier
X
X
What if we were to simply treat this as opaque data, interpreted by packet processing functions as needed?
Could we treat the address field as just another input to processing, much like telephone calls are just another app on a smartphone?

## Slide 11: The Advantages of Opacity
We are not constrained by a pre-conceived notion of the size of the address.
  For some applications 20, 32, 48, or 128 bits are too small.
  Equally for some applications such sizes are too large
We are not constrained by any predetermined mapping of an address to an action.
We have a model to introduce new functionality to the network layer
We have a new dimension to network security, or at least the application of the MPLS security model to a richer set of applications.

## Slide 12: Research Questions
What types of innovation would be unleashed by unshackling the address semantics?
Is this a path that allows networks to become as programmable as applications?
What other functions can we map to address?
What other types of cardinality are useful?
Do the same considerations apply to the underlay, overlay and the end-user application?
How do we achieve aggregability of addressing with opaque addresses?
What would be its implications, from efficient hardware support to late binding of semantics?

## Slide 13
Questions?